## Slide 1: Hello world kernel module
Giảng Viên: Lưu An Phú

## Slide 2: Agenda
Introduction
Setup environment for development
Create Hello world kernel module
Home work

## Slide 3: Introduction
Can extend kernel code when needed
Interact with kernel to become only one kernel process
Code instruction has same priority with kernel

## Slide 4: Install kernel header in Ubuntu
It include all source header need to develop kernel module
It is generate when they build kernel image
Each kernel instance has only one kernel header
Apt-get install linux-headers-$(uname -r)

## Slide 5
Final result

## Slide 6
Create Hello world kernel module

## Slide 7: Source code

## Slide 8: Compile kernel module
Create makefile to compile
make

## Slide 9: Check log in kernel
Sử dụng command dmesg để get log từ kernel.

## Slide 10
Kernel module for beagle bone

## Slide 11: Hardware
Board
  Beaglebone black.
  8g sd card.
Connector
  Cp2102.

## Slide 12: Firmware
Download firmware from main page
  https://beagleboard.org/latest-imagesInstall firmware
Format sdcard, write firmware to sdcard.
  sudo dd if=NameOfImageToWrite.img of=/dev/rdiskNUMBER bs=1m
Plug in sdcard, power cable, mouse, keyboard and monitor for Pi

## Slide 13: Connect PC with board
Install MobaXterm for PC
  https://mobaxterm.mobatek.net/
Setup MobaXterm to connect with beagle bone.

## Slide 14: Cross compile kernel module
Trong các dự án embedded Linux mọi người rất ít khi build source code trên board. Thay vào đó họ thường build source code trên PC, copy file execute sang board và chạy. Kỹ thuật đó gọi là cross compile.
https://blukat29.github.io/2017/12/cross-compile-arm-kernel-module/

## Slide 15: Cross compile kernel module
Source code linux kernel cho board.

## Slide 16: Home work
Kết nối đèn led với chân GPIO của board. Đọc RM để biết cách cài đặt chân GPIO của board. Viết 1 kernel module để mỗi khi load lên sẽ bật đèn led, unload sẽ tắt đèn led.
  Tham khảo các hàm sau:
    devm_ioremap_resource
    __raw_writel
    https://youtu.be/3MY8kLEZr98

## Slide 17: Thank you